## Slide 1: DryFiningTM Technology
Notes: 1
I am briefly going to describe a commercially available technology developed and patented by GRE which is being used on coal consumed 2 of our coal plants in ND. The technology involves an innovative use of waste heat to reduce moisture in the coal prior to combustion as well as a segregation technology removing higher density impurities in the coal prior to combustion. These two improvements (moisture removal and contaminant removal through segregation) primarily using waste heat is increasing plant efficiency, decreasing air emissions and saving the plant money in O&M costs through less wear and tear.

## Slide 2: DryFiningTM improvements
NOx
Contaminant
Removal
Less Moisture and
Contaminants means:
Notes: 100 tons go into the coal dryer. In the first stage, 10 tons are segregated by density and go to the air jigs for removal of the heavier material (pyrites, clays, etc.). One ton is segregated out and disposed of in the ash ponds. The other nine tons are either sent to Spiritwood, or put back in the dried coal stream for use at Coal Creek. Of the 90 tons that remain in the dryer, eight tons of water are removed and go up the stack as vapor. This leaves 82 tons of coal dryer product, 91 tons if the air jig product is not going to Spiritwood, for consumption in the CCS boilers

## Slide 3
How it works
Notes: 100 tons go into the coal dryer. In the first stage, 10 tons are segregated by density and go to the air jigs for removal of the heavier material (pyrites, clays, etc.). One ton is segregated out and disposed of in the ash ponds. The other nine tons are either sent to Spiritwood, or put back in the dried coal stream for use at Coal Creek. Of the 90 tons that remain in the dryer, eight tons of water are removed and go up the stack as vapor. This leaves 82 tons of coal dryer product, 91 tons if the air jig product is not going to Spiritwood, for consumption in the CCS boilers

## Slide 4: DryFining impacts
  10% less fuel – reduces O&M on fuel handling
  54% less SO2 - Segregation of ash minerals, plus improved collection efficiency
  40% less Hg- Segregation of ash minerals, plus improved collection efficiency
  32% less NOX- Reduced volumetric release rate, improved air & fuel distribution to furnace
  4% less CO2- 4% improved cycle efficiency
  $20+ million in annual O&M savings

## Slide 5: Efficiency improvement
Chart: 
| Reduce Air Heater Leakage (6% to 1%) | Low-T Feedwater Pre-heating | Low-T Air Pre-heating | Reduce cooling tower approach temperature | Natural Draft Cooling Tower | Dual Reheat | Ultra-SuperCritical at 1120F/1120F (604C/604C) | Low-T Fuel Drying | Ultra-SuperCritical at 1250F/1292F (680C/700C) | Advanced Ultra-Supercritical at 1350F/1400F (732C/760C)
 | 0.001 | 0.002 | 0.006 | 0.007 | 0.0075 | 0.0175 | 0.02 | 0.04 | 0.0975 | 0.1375

## Slide 6: DryFining results at Coal Creek
Conferences, journal articles & awards
Marketing agreements:
  Black & Veatch
  In discussion with others
International recognition

## Slide 7
Thank you!